Landmark based shortest path detection in alarm system

Nadia Mahmood Hussein Department of Computer Science,, College of Science, Almustansiriyah University -Baghdad - Iraq nadia.salam97@yahoo.com Saad Najim AlSaad Department of Computer Science, College of Science, Almustansiriyah University -Baghdad -Iraq alsaad6060@ gmail.com

Abstract-      In this paper, an alarm system for four types of emergency states (explosion, car accident, earthquake and fire) is developed. This system divided in to two parts: transmitted part (Arduino, sensors, GSM, GPS), and emergency part (center site, sub center sites). Center site is included (Android phone, Server), Sub center sites (helping centers) represented the mobile phones of competent authorities like police center or hospital. The alerting in this system as a SMS message is sent by GSM. The system used Haversine formula to determine the nearest sub center from emergency state that receives the SMS alarm message from transmitted part. Also the path is tracked using Google map application.

الخلاصة

في هذه البحث، تم تطوير نظام إنذار لأربعة أنواع من حالات الطوارئ (الانفجار، حادث سيارة، الزلزال الحريق). وينقسم هذا النظام إلى جزأين: الجزء المتنقل (اردوينو، وأجهزة الاستشعار، النظام العالمي للاتصالات المتنقله ، نظام المواقع العالمي)، وجزء الطوارئ (الموقع المركزي، المواقع فرعيه). الموقع المركزي يتضمن (هاتف الاندرويد,الخادم)، المراكز الفرعية (مركز مساعدة) تمثل الهواتف النقالة للسلطات المختصة مثل مركز الشرطة أو المستشفى. يتم إرسال التنبيه في هذا النظام كرساله قصيره بواسطة النظام العالمي للاتصالات المتنقله. استخدم النظام صيغة هافرسين لتحديد أقرب مركز فرعي من حالة الطوارئ التي تتلقى رسالة التنبيه القصيره من الجزء المتنقل. كما يتم تتبع المسار باستخدام تطبيق خريطة جوجل.

Keyword: - Arduino, GSM, GPS, Proteus, Google map, Haversine.

- Introduction

No one can prevent the accident. The accidents and emergency situations are frequently occurred .These accidents are either natural events such as earthquakes and floods or those that are caused by someone, such as explosions and car accidents. All these situations need rapid intervention by competent authority to reduce the resulting losses in human life by reducing as possible the time between the moment of problem occurrence and the moment of arrival the competent authority to give assistant.

The most important parameter of any alarm system is its reliability in performing its designated task, in addition to all such systems must be difficult to disable, easy to use and have good immunity against malfunctioning [1]. In this paper, we design and implement a system that alert automatically when an accident is occurred. To make the system works in real time and accurate, it needs to include the supporting technologies like Global Positioning System (GPS) and Global System for Mobile Communications (GSM) technologies. GPS is used to retrieve the position of the vehicle in form of latitude and longitude coordinates, and GSM as a medium of data communication between the transmitted part and emergency part. This system suggested an important way to reduces as possible the losses by inform the nearest center to the problem by using haversine formula. Many researchers are applied this formula in their works. Ganesh and Vijaya Kumar are applied haversine to find the distance between two points and find the location of object inside the building with better accuracy [2]. Arup Kumar Bhattacharjee and Soumen Mukherjee are used haversine to calculate distance between a customer and a store as well as compare distance with nearest store’s geographical area [3]. Rajib Chandra Das and Tauhidul Alam are applied haversine to calculate the distance between current location of the user and location of nearest healthcare center in a system [4].

- System requirement

The general idea of the proposed system is depicted in figure 1.The system consist of two parts Transmitted part and emergency part. We will go in details in the next section.

Fig 1: The whole proposed system

The hardware and software requirement are abstracted in Table1.

| H.W Requirement | S.W Requirements |
| --- | --- |
| Microcontroller Arduino UNO GSM (Global System for Mobile ) GPS ( global positioning system ) Sound sensor Fire detector Shock sensor ADXL335 Accelerometer Jumper Wires Bread board Resistance Cable to connect Arduino to Pc Led SIM Pc Android mobile | Arduino c language C# 2012 SQL 2012 Mymobikit |

Table 1: H.W & S.W Requirements

.

  - Arduino microcontroller

A micro-controller is a small computer on a single integrated circuit containing a processor core, memory, and programmable input/ output peripherals .Arduino Uno is an open-source single-board microcontroller, designed to connect to electronics and control them. It is able to make decisions of what to do base off of input from the outside world. Open source Arduino software is Integrated Development Environment (IDE). One of the best parts about Arduino is needed to program the boards [5] [6].

  - Sound sensor

The Sound sensor module is a simple microphone. Based on the power amplifier and electret microphone, it can be used to detect the sound strength of the environment [7].

  - Shock Sensor

The sensor that used to detect accident, it detects any hard impact acted on it. These sensors are distributed on all sides of the car to detect the impact. The output values of all sensors are sending into OR gate to detect at least one impact [8].

  - Temperature sensor

Sensor LM35 will constantly send the temperature values to Arduino. It check the temperature value , If  it  is above a certain level, say 50°C, Arduino unit will trigger an alarm and sends an warning  message to fixed center through GSM.[9].

## ADXL335 Accelerometer

The ADXL335 is a complete 3-axis acceleration measurement system. The accelerometer can measure the static acceleration of gravity in tilt-sensing applications as well as dynamic acceleration resulting from motion, shock, or vibration [10]. In this system used to detect the earthquake state.

  - GSM (Global System for Mobile)

Global system for mobile communication is digital mobile telephony system and completely optimized for full duplex voice telephony. GSM modem is a specialized type of modem requires a SIM card provided by a network operator to interface with the cellular network [12]. Arduino GSM shield will be used in this system.

  - GPS (global positioning system)

Global Positioning System (GPS) is a satellite based, medium earth orbit (MEO), navigation technology. GPS provide location, speed and direction information to its users this information collected by at least 24 satellites. GPS have very low accuracy in the cities which have high buildings and narrow streets because the limited number of satellites that found [13]. In this system used GPS in transmitted part to get the coordinate of the vehicle.

- System design

The aim of the paper is to find out the shortest path between event place and helping center site (hospital, police center) using GPS technology. The mechanism of the work is started from transmitted part. When the sensors sense the problem, GPS get the location from satellite. GSM will send SMS message to emergency part. Arduino microcontroller is controlled on all these modules (Sensors, GPS, and GSM). These modules need embedded language to give its designed goal. Assembly C language is implemented as powerful tool for supporting helping these modules to work efficiently. The task of Emergency part is receiving the SMS. Figure 2 illustrate the contained of message .The message is started with alarm word then type of event (explosion, car accident, earthquake, fire) and the location of event as (latitude and longitude).

Fig 2: Alarm message

The SMS is sent to server by using web services technologies. Data base of all the real location (latitude, longitude) of helping center site and its phone number. Haversine formula is used to find the shortest path between locations that taken by GPS and locations in database. The alarm message will be sent to nearest helping center and the shortest path will be view in Google map application.

3.1 Havesine formula

The earth has a spherical shape but it is not a flat disk, so we should be taking this into account when we need to computing distances between two positions on a sphere. A line along a sphere is longer than a straight line that connects two points crossing the sphere [14]. There are four different methods to calculate distance between any two geographical points. These are, the 'Spherical law of cosines', 'Haversine', 'Vincenty Sphere' and ' Vincenty Ellipsoid' (Vincenty, 1975) methods. The 'Vincenty Ellipsoid' assumes the earth to be  an ellipsoid  while others  assume it is a Sphere [15]. Haversine Formula gives minimum distance between any two points on a sphere. It is an important equation in navigation, giving great-circle distances between any two points from their longitudes and latitudes [16]. Haversine formula was employed for calculating the distances between event location and the nearest sub center. Figure 2 describes the pseudo coding to compute the distance between two locations p1 and p2 using Haversine. Each p1 and p2 are given as latitude and longitude.

Pseudo coding1:  Perfom Haversine formula

Input :  point P1(lat1, lon1), point p2(lat2, lon2)

R= earth’s radius (radius = 6,371km)

Output : d // the distance between p1 and p2

Begin

Δlat = lat2 − lat1

Δlon = lon2 − lon1

End .

The proposed system computation to find the nearest helping center is presented is presented in Algorithm 1.

Algorithm 1: Finding Nearest Helping Center

Input:  eventlocation // location of event // (latitude, longitude).

Helpcenters// array of all locations of helping centers in Data base of all

Output : pos // location of nearest helping center

Begin

Step 1 For i= 1 to no. of helping centers in database

D(i) =  heversine (helpentecnter(i) , evenlocation)

Step2 :- pos = minimum (D)

End

Table 2 shows an illustration example of the algorithm of five police centers in database and an accident location is 33.374436, 44.384382. The nearest center is the Cairo Police Station.

| Haversine distance | Lon Coordinate Lon(i) | Lat Coordinate Lat (i) | Helping center Name |
| --- | --- | --- | --- |
| 5910,47 | 44.388478 | 33.352610 | Bab Al - Mu'adh Police Station |
| 5908.916 | 44.423145 | 33.362848 | Al- Kana Police Station |
| 5916.267 | 44.437466 | 33.294581 | Al- karadah Police Station |
| 5906.267 | 44.387146 | 33.386373 | Cairo Police Station |
| 5906.483 | 44.362891 | 33.391616 | Al - Sulaikh Police Station |

Table 2: Haversine distance.

- Simulations Results

Proteus software is one of the important software that used in simulation and especially in microcontroller simulation, schematic capture, and printed circuit board (PCB).It is used to get the beginning result for any project and for testing the circuit and check if a system is working successfully. The sensor that used in the proposed system is checked using Proteus software. Figure 3 shows the circuit with description for each component.

Fig 3: Temperature sensor simulation,

If  the tempruture degree >= some threeshold as example 55°C then the sensor will give a signal to arduino and a worning message will apper, othorwise if  the tempruture degree < 55°C then no thing occurs.Figure 4a & 5b  shows the runing of project.

)a)                                                                            (b)

Fig 4: a- Running of the project.

b- Virtual terminal result

- Result and discussions

In this system, haversine solves a big problem by quickly response from nearest sub center and thus decrease the number of victims and the value of losses. Figure 5 shows the nearest path between the place of event and the place of helping center using Google map application. Also the proposed system gives alternative paths as shown in figure 5. Our objective have been achieved and the maximum time that need from the moment of accident occurrence and the moment of intervene in worst case is 20.5 second, and minimum time is 10.5 second in best case. This time is very optimal for alarm systems to decrease the casualties and for fast response.

Fig 5: Shortest and alterative paths.

- Conclusion

Hence, Haversine formula is used to determine the nearest sub center from accident place using GPS technology. Also, Microcontroller will be used to develop a smart emergency system that alert emergency center remotely. The system sends SMS alarm to emergency center that analysis and monitoring the events also send the alarm to nearest helping center and display the path on Google map application. Proteus software is used to test the system and check the result. Decrease the victims and loss is the main constraint of this work. The system can be easily implemented with high reliability, high security and low cost.

- References

| [1] | Marston, Raymond Michael. "Security Electronics Circuits Manual". Book, Newnes,1998.‏. |
| --- | --- |
| [2] | Ganesh L1, DR. Vijaya Kumar B P2." Indoor Wireless Localization using Haversine Formula". International Advanced Research Journal in Science, Engineering and Technology,2015. |
| [3] | Arup Kumar Bhattacharjee, et al. "Personalized Promotion Tracking: A Location Based Approach for Merchandizing Industry using Haversine Formula" International Journal of Science, Engineering and Management (IJSEM) , 2016. |
| [4] | Rajib Chandra Das and Tauhidul Alam. " Location Based Emergency Medical Assistance System Using OpenStreetMap", 3rd International Conference on Informations, Electronics & Vision, 2014. |
| [5] | Smith, Alan G. "Introduction to Arduino." Reference book, September 30 (2011). |
| [6] | Amariei, Cornel. Arduino Development Cookbook. Packt Publishing Ltd, 2015.‏ |
| [7] | Jiankai.li, Sound sensor user manual, seeed Grow the di_erence, 2015. |
| [8] | Jazim Baramy and et al . "Accident Detection & Alerting System", International Journal of Technical Research and Applications, 2016. |
| [9] | Vaibhav Sharma and et al ." Advanced Low Cost Security System Using Sensors, Arduino and GSM Communication Module", Proceedings of IEEE TechSym 2014 Satellite Conference, VIT University, 7th-8th March. |

[10] Devices, Analog. "Small, Low Power, 3-Axis±3 g Accelerometer ADXL335" , (2009).‏

[11] Miceli, Andrew. "Wireless technician's handbook", 2nd, Artech House, 2003.‏

[12] Al Jhawari, Fatema Rashid, and T. Sheeba. "Location based Alarm using Mobile Device."‏ International Journal of Computer Applications 2014.

[13] Hermsen, Harm. "Using gps and accelerometer data for rowing race tracking." U.      o. G. Artificial Intelligence Dept of Artificial Intelligence, Master Thesis , Ed.,ed (2013).‏

[14] Hijmans, Robert J., E. Williams, and C. Vennes. "The” geosphere” package    (Version 1.5. 5)." (2016).‏

[15] Ingole, P. V., and Mr Mangesh K. Nichat. "Landmark based shortest path detection by using Dijkestra Algorithm and Haversine Formula."International Journal of Engineering Research and Applications 3, (2013).‏